## Slide 1: Chapter 2
Instructions: Language of the Computer

## Slide 2: Instruction Set
The repertoire of instructions of a computer
Different computers have different Instruction sets
  But with many aspects in common
Early computers had very simple instruction sets
  Simplified implementation
Many modern computers also have simple instruction sets
§2.1 Introduction

## Slide 3
ISA - what it includes?
  Instruction Set and Instruction Formats
  Modes of Addressing
    Accessing Data Items and Instructions
  Exceptional Conditions handling
  Characteristics and Choreography of principle functional units (ALU, Registers, RAM etc.)
  Information flows between such components and the control logic of such information flows
  Register Transfer Language (RTL) Description

## Slide 4
Example ISAs
Digital Alpha (v1, v3) 1992-97
HP PA-RISC (v1.1, v2.0) 1986-96
Sun Sparc (v8, v9) 1987-95
SGI MIPS (MIPS I, II, III, IV, V) 1986-96
Intel (8086,80286,80386, 1978- 80486,P-P4, MMX,
Celeron, Ppro, Xeon,
IA-32, IA-64, I7)
We will focus on MIPS ISA

## Slide 5
ISA - Design Issues
Can it be implemented? Cost and time?
Can it be programmed? Ease of compilation?
Instruction length /program length in memory?
Number of instructions need to be executed?
How many clocks required per instruction?
Bytes flow from Main memory to CPU?
NOTE: this also depends on instructions set, processor organization, and
compilation techniques.

## Slide 6: The MIPS Instruction Set
Used as the example throughout the book
Stanford MIPS commercialized by MIPS Technologies (www.mips.com)
Large share of embedded core market
  Applications in consumer electronics, network/storage equipment, cameras, printers, …
Typical of many modern ISAs
ARM
  See MIPS Reference Data tear-out card, and Appendixes B and E

## Slide 7: MIPS ISA
ISA is an abstraction of Machine code- it is the Language of the Machine
More primitive than higher level languages e.g. no sophisticated control flow and very restrictive instructions
MIPS is similar to other architectures developed since the 1980's
MIPS is used by NEC, Nintendo, Silicon Graphics, Sony , AMD
Goal: maximize performance, minimize cost,
reduce design time

## Slide 8: MIPS- special features
MIPS is a RISC, a compact and simple ISA
Instruction length is fixed - 32 bits
Simple Instruction Formats- 3 Types [ R-I-J formats]
Register file is small- 32 32-bit GPR
Reg-Reg 3 address arithmetic format
Only LW and SW can access main memory
LW and SW has only base+displace address
Simple Branching (bne and beq only)
Delayed Branch etc.
Simple Implementation  low power, less heat

## Slide 9
Typical Machine Operations
Data Movement
Load (from memory)
Store (to memory)
memory-to-memory move
register-to-register move
input (from I/O device)
output (to I/O device)
push, pop (to/from stack)
Arithmetic
integer (binary + decimal) or FP
Add, Subtract, Multiply, Divide
Logical
not, and, or, set, clear
Shift
shift left/right, rotate left/right
Control (Jump/Branch)
unconditional, conditional
Subroutine Linkage
call, return
Interrupt
trap, return
Synchronization
test & set (atomic r-m-w)
String
search, translate
Graphics (MMX)
parallel subword ops (4 16bit add)

## Slide 10
Typical Top 10 Instructions

## Slide 11
Main Machine Instructions
Support at least these simple but more frequent instructions in ISA, since they will dominate the number of instructions executed:
  add, subtract
  load, store
  move register-register
  and
  shift
  compare equal, compare not equal
  branch, jump
  call & return

## Slide 12
R – Format
Instructions
Arithmetic: ADD, SUB, ..
Logical: AND, OR, …
Other: SLT, ……
R[rd]  R[rt] op R[rs]

## Slide 13: Arithmetic Operations
MIPS Assembly code
Add and subtract, three operands
  Two sources and one destination
add a, b, c # a gets b + c
All arithmetic operations have this form
Design Principle 1: Simplicity favors regularity
  Regularity makes implementation simpler
  Simplicity enables higher performance at lower cost
§2.2 Operations of the Computer Hardware

## Slide 14: Arithmetic Example
C code:
f = (g + h) - (i + j);
MIPS Assembly code:
add t0, g, h # temp t0 = g + h add t1, i, j # temp t1 = i + j sub f, t0, t1 # f = t0 - t1

## Slide 15: MIPS ISA - ADD
Example: C code: A = B + C
MIPS Assembly add A, B, C
-No variable names in Machine Code
- Assembler associate registers with variables, A in $s0, …
MIPS ISA: add $s0, $s1, $s2
A- $S0 or $16
MIPS Machine Code:
0000010001100101000000000100000
000000
10001
100000
10010
10000
00000

## Slide 16
R-type - ADD
C code: A = B + C
MIPS code: add $rd, $rs, $rt
6
000000
rs
100000
rt
rd
-
fields
bits
5
5
5
5
6
ADD-32
Registers
Control
ADD
Assume
B and C are already loaded into $rs and $rt respt.
The result B+C will be stored into $rd

## Slide 17: Simplicity favors regularity !
All MIPS instruction are 32 bits long
MIPS have only 3 instruction formats
All operands are registers (GPRs) or immediate values
Operand order is fixed (destination last)

## Slide 18
General Purpose Registers (GPR)
All machines use GPR Since 1975
Registers are in chip - faster than memory
Flexible for a compiler to use - even in parallel
e.g., (A*B) – (C*D) – (E*F) do multiplies in any order
Memory traffic is reduced- program is sped up
Code density improves - named with fewer bits
Spilling- if it can’t hold all variables,
  ‘spilled’ to main memory (eg. array, fn call]
°
•
-

## Slide 19
MIPS: Software conventions for Registers
0 zero constant 0
1 at reserved for assembler
2 v0 expression evaluation &
3 v1 function results
4 a0 arguments
5 a1
6 a2
7 a3
8 t0 temporary: caller saves
. . . (callee can clobber)
15 t7
16 s0 callee saves
. . . (caller can clobber)
23 s7
24 t8 temporary (cont’d)
25 t9
26 k0 reserved for OS kernel
27 k1
28 gp Pointer to global area
29 sp Stack pointer
30 fp frame pointer
31 ra Return Address (HW)
In ISA-Registers will be indicated by
$0 (or $zero) , $1 [or $at], and so on..

## Slide 20: Smaller is faster !
Only 32 registers provided.
  This decrease complexity of the design
  increase execution time
  only 5 bits are needed for naming them
MIPS Registers are pre-allocated for different tasks
E.g $0=0,
$1 – for assembler, etc.

## Slide 21: The Constant Zero
MIPS register 0 ($zero) is the constant 0
  Cannot be overwritten
Useful for common operations
  E.g. 1: move between registers
  add $t2, $s1, $zero (R[t2]  R[s1])
  move $t2, $zero (assembly)
  E.g.2: to load immediate value in a register
  ori $t1, $0, 5 ( R[t1]  5 )
  li $t1, 5 (assembly)

## Slide 22: MIPS R-format Instructions
Instruction fields
  op: operation code (opcode)
  rs: first source register number
  rt: second source register number
  rd: destination register number
  shamt: shift amount (00000 for now)
  funct: function code (extends opcode)
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits

## Slide 23: R-format Example
add $t0, $s1, $s2
special
$s1
$s2
$t0
0
add
0
17
18
8
0
32
000000
10001
10010
01000
00000
100000
000000 – Distinguishes R-Type from other types
100011001001000000001000002 = 0232402016
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits

## Slide 24
R-type – ADD & SUB
C code: A = B + C
MIPS code: add $16, $17, $18
6
0
17
32
18
16
-
fields
bits
5
5
5
5
6
MIPS Machine Code :
For subtraction, function code is 34
+ and - differs only on one bit- easy for implementation
000000
10001
100000
10010
10000
00000
For all arithmetic operation op-code is zero.
000000
10001
100010
10010
10000
00000

## Slide 25: RTL – Register Transfer Language
add $rd, $rs, $rt
R[rd]  R[rt] + R[rs]

## Slide 26
R-type - Arithmetic
C code: A = B op C
MIPS code: op $rd, $rs, $rt
6
000000
rs
fnCode
rt
rd
-
fields
bits
5
5
5
5
6
ADD-32 SUB-34
Registers
Control
ADD-?? SUB-??

## Slide 27: R-Type: Logical Operations
Instructions for bitwise manipulation
Operation | C | Java | MIPS
Shift left | << | << | sll
Shift right | >> | >>> | srl
Bitwise AND | & | & | and
Bitwise OR | ¦ | ¦ | or
Bitwise NOT | ~ | ~ | nor
Useful for extracting and inserting groups of bits in a word
§2.6 Logical Operations

## Slide 28: Shift: Logical (SLL & SRL)
shamt: how many positions to shift
Shift left logical ($rs not used)
  Shift left and fill with 0 bits
  sll by i bits multiplies by 2i
Shift right logical
  Shift right and fill with 0 bits
  srl by i bits divides by 2i (unsigned only)
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits

## Slide 29: Shift: Arithmetic (SRA only)
Arithmetic shift is relevant when shifting 2’s compliment numbers right only.
SRA : Shift right arithmetic- MSBs will be filled with the sign bits- not zeros [divides by 2i
  Shift right and fill with MSB bit
There is no SLA in MIPS
  Overflow possible
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits

## Slide 30: Shift- Logical Vs Arithmetic
SRL
SLL
SRA
SLA
not available
sign-bit will be lost

## Slide 31: More on Shift
sll Shift left logical by a constant number of bits (immediate value)
sllv Shift left logical by a variable number of bits
srl Shift right logical by a constant number of bits
srlv Shift right logical by a variable number of bits
sra Shift right arithmetic by a constant number of bits
srav Shift right arithmetic by a variable number of bits
sll $rd, $rt, shift_amt ($rs not used)
sllv $rd, $rt, $rs ($rs has the shift amount)
srl $rd, $rt, shift_amt
srlv $rd, $rt, $rs
sra $rd, $rt, shift_amt (arithmetic shift- sign?)
srav $rd, $rt, $rs

## Slide 32: Shift
Instruction | B31-26 | B25-21 | B20-16 | B15-11 | B10-6 | B5-0
 | opcode | register s | register t | register d | shift amount | function
sll $rd, $rt, shift_amt | 000 000 (SPECIAL) | unused | - | - | shift_amt | 000 000
sllv $rd, $rt, $rs | 000 000 (SPECIAL) | - | - | - | 00000 | 000 100
srl $rd, $rt, <shift_amt> | 000 000 (SPECIAL) | unused | - | - | shift_amt | 000 010
srlv $rd, $rt, $rs | 000 000 (SPECIAL) | - | - | - | 00000 | 000 110
sra $rd, $rt, <shift_amt> | 000 000 (SPECIAL) | unused | - | - | shift_amt | 000 011
srav $rd, $rt, $rs | 000 000 (SPECIAL) | - | - | - | 00000 | 000 111
representations for bitshift logical operators.

## Slide 33: AND Operations
Useful to mask bits in a word
  Select some bits, clear others to 0
and $t0, $t1, $t2
0000 0000 0000 0000 0000 1101 1100 0000
0000 0000 0000 0000 0011 1100 0000 0000
$t2
$t1
0000 0000 0000 0000 0000 1100 0000 0000
$t0

## Slide 34: OR Operations
Useful to include bits in a word
  Set some bits to 1, leave others unchanged
or $t0, $t1, $t2
0000 0000 0000 0000 0000 1101 1100 0000
0000 0000 0000 0000 0011 1100 0000 0000
$t2
$t1
0000 0000 0000 0000 0011 1101 1100 0000
$t0

## Slide 35: NOT Operations
Useful to invert bits in a word
  Change 0 to 1, and 1 to 0
MIPS has NOR 3-operand instruction
  a NOR b == NOT ( a OR b )
nor $t0, $t1, $zero
0000 0000 0000 0000 0011 1100 0000 0000
$t1
1111 1111 1111 1111 1100 0011 1111 1111
$t0
Register 0: always read as zero

## Slide 36: R- Format: ISA encoding Examples
add $16,$2,$15
sub $16,$2,$15
add
0
2
15
16
0
32
sub
0
2
15
16
0
34
add and sub differ only by one bit
and $16,$2,$15
or $16,$2,$15
sllv $16,$2,$15
srlv $16,$2,$15
slt $16,$2,$15
and
0
2
15
16
0
36
or
0
2
15
16
0
shl
0
2
15
16
shr
0
2
15
16
addu $16,$2,$15

## Slide 37
R-type - General
C code: A = B op C
MIPS code: op $rd, $rs, $rt
6
000000
rs
fnCode
rt
rd
?
fields
bits
5
5
5
5
6
ADD-? ADDU - ? SUB-? AND-? OR - ?
Registers
Control
SLT - ?

## Slide 38
I- Format
Instructions
Immediate Value Included
In the statement.
Data Transfer: LW, SW
Arithmetic with Immediate: addI, …
Conditional Branching
Do-While Loop

## Slide 39
Immediate
Arithmetic

## Slide 40: Immediate Operands
Design Principle 3: Make common case fast
  Small constants are common (e.g. for loop)
  Immediate operand avoids a load instruction
Constant data specified in an instruction
addi $s3, $s3, 4
  No subtract immediate instruction
    Just use a negative constant
  addi $s2, $s1, -1

## Slide 41: Immediate Arithmetic
addi $rd, $rs, $rt
6
op
rs
funct
rt
rd
shamt
fields
bits
5
5
5
5
6
op field is special purpose and already allocated
funct code depend on op field - may be reallocated
To keep R- format, I may get maximum 6 bits only
Immediate value +/- 32 is NOT SUFFICIENT
Can we use R-format?

## Slide 42: MIPS I-format Instructions
Design Principle 4: Good design demands good compromises
  Compromise uniqueness- introduce a new type
    Different formats complicate decoding,
    but allow 32-bit instructions uniformly
  Keep formats as similar as possible
Immediate arithmetic and load/store instructions
  rt: destination or source register number
  Constant: Represented as a 16-bit 2’s complement
    Range of I is –215 to +215 – 1
  (next) Address: offset added to base address in rs
op
rs
rt
I- constant (or address)
6 bits
5 bits
5 bits
16 bits

## Slide 43: Logical Immediate Operations
Instructions for bitwise manipulation
Operation | C | Java | MIPS
Bitwise AND | & | & | andi
Bitwise OR | ¦ | ¦ | ori
Bitwise XOR | ~ | ~ | xori
ori $16, $0, 5 (what will happen?)
li $16, 5 (is this pseudo?)
§2.6 Logical Operations

## Slide 44
DATA TRANFER

## Slide 45: Memory Operands
Main memory used for composite data
  Arrays, structures, dynamic data
To apply arithmetic operations
  Load values from memory into registers
  Store result from register to memory
Memory is byte addressed
  Each address identifies an 8-bit byte
Words are aligned in memory
  Address must be a multiple of 4
MIPS is Big Endian
  Most-significant byte at the least address of a word
  c.f. Little Endian: least-significant byte at least address

## Slide 46: Memory Organization
Viewed as a large, single-dimension array.
A memory address is an index
into the array
"Byte addressing" means that the
index points to a byte of memory.
MIPS words are 32 bit long
MIPS can address 232 bytes
or 230 words (what are 2 lsb’s ?]
...
0
1
2
3
4
5
6
8 bits of data
8 bits of data
8 bits of data
8 bits of data
8 bits of data
8 bits of data
8 bits of data
0
4
8
12
...
32 bits of data
32 bits of data
32 bits of data
32 bits of data
Alignment: require that objects fall on
address that is multiple of their size.
Can’t address in middle.
Always MIPS address has two zero lsb

## Slide 47: Registers vs. Memory
Registers are faster to access than memory
Operating on memory data requires loads and stores
  More instructions to be executed
Compiler must use registers for variables as much as possible
  Only spill to memory for less frequently used variables
  Register optimization is important!

## Slide 48: Big Vs Little Endian
MIPS & Networks use Big Endian
Similar to Left to Right reading
Intel- X86 use Little Endian
LLL rule : Little-Low-Least
Example: 0000 1010 0000 1011 0000 1100 0000 1101

## Slide 49: Memory Operand Example 1
C code: g = h + A[8];
  g in $s1, h in $s2, base address of A in $s3
Compiled MIPS code:
  Index 8 requires offset of 32
    4 bytes per word
lw $t0, 32($s3) # load word add $s1, $s2, $t0
offset
base register

## Slide 50: Memory Operand Example 2
C code:
A[12] = h + A[8];
  h in $s2, base address of A in $s3
Compiled MIPS code:
  Index 8 requires offset of 32
lw $t0, 32($s3) # load word add $t0, $s2, $t0 sw $t0, 48($s3) # store word

## Slide 51: Data Transfer Instructions
C code: A[8] = A[8]+ h; h is in $s2 MIPS code: lw $t0, 32($s3) ; A’s base in $s3 add $t0, $s2, $t0 ; h is in $s2 sw $t0, 32($s3)
General format - STORE WORD sw rt , offset(rs)
effect is mem [rs + offset]  rt
where rs contain base address, and
offset is an immediate value
General format - LOAD WORD lw rt , offset(rs)
effect is rt  mem [rs + offset]
  Store word is destination first ?

## Slide 52: Data Transfer Instructions
Only two types of Data transfer (Mem Reg]
Only two (Load / Store] can access main memory.
Use only one addressing mode, base+offset
sw rt, I(rs)
lw rt, I(rs)
Why not R-format? I may get max 6 bits only
  Array size 64 is not sufficient for programs
I-format is good- it allows 16 bits for offset
I- format is used.
6
op
rs
I
rt
fields
bits
5
5
16
  OP-codes; lw: 35, sw:35+8

## Slide 53: LW & SW: Example-3
add $8,$5,$5
add $8,$8,$8
add $8,$4,$8
lw $16, 4($8)
sw $16, 0($8)
v[k] = v[k+1];
Compiler already placed the value k in $5 and
array v’s start address on $4
First two instructions calculates 4 * k (in R[8]).
Next, v[k]’s position is calculated; v + 4k (in R[8])
Next, load word from v[k+1] to R[16].
Next, store word from R[16] to v[k]
  Write MIPS codes; op-codes; lw: 35, sw:35 +8
6
op
rs
I
rt
5
5
16

## Slide 54: LW & SW: Example- 4: SWAP
add $8,$5,$5
add $8,$8,$8
add $8,$4,$8
lw $15, 0($8)
lw $16, 4($8)
sw $16, 0($8)
sw $15, 4($8)
int temp;
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
Compiler already placed the value k in $5 and
array v’s start address on $4
Compiler allocates space for the variable temp in
register 15

## Slide 55: I-format ISA encoding
lw $15, 20 ($2)
sw $15, 20 ($2)
add $16,$2,$15
addi $15, $2, 20
sub $16,$2,$15
35
2
15
20
lw
43
2
15
20
sw
8
2
15
20
addi
add
0
2
15
16
0
32
sub
0
2
15
16
0
34
100011
00010
011111
0000000000010100
lw
101011
00010
01111
0000000000010100
sw
001100
00010
01111
0000000000010100
addi
add
000000
00010
01111
10000
00000
100000
sub
000000
00010
01111
10000
00000
100010
lw and sw differ only by one bit

## Slide 56
CONDITIONAL
BRANCING

## Slide 57: Basic Blocks
A basic block is a sequence of instructions with
  No embedded branches (except at end)
  No branch targets (except at beginning)
A compiler identifies basic blocks for optimization
An advanced processor can accelerate execution of basic blocks

## Slide 58: Stored Program Concept & Conditional Branch & PC & IR
Instructions are 32 – bits binary encoded numbers
Programs are stored in memory — to be read or written just like data
A special register PC contains the address of the next instruction-usually the next one to the current being executed (PC  PC+4]
A special register IR contains the current instruction being executed (not always)
A branch instruction may change PC, PC  PC + ?
Branch gives the power and challenge.

## Slide 59: Stored Program Computers
Instructions represented in binary, just like data
Instructions and data stored in memory
Programs can operate on programs
  e.g., compilers, linkers, …
Binary compatibility allows compiled programs to work on different computers
  Standardized ISAs
The BIG Picture

## Slide 60: Fetch & Execute Cycle
  PC gives address of next instruction
  Instructions are fetched and put into a special register IR
  And then PCPC+4
  Bits in the register IR "control" the subsequent actions.
  A branch or jump instruction may change PC again
  Fetch the “next” instruction (address of it is in PC now] and continue
New PC value
PC
Memory
IR
4
+
instruction
address
A Multi-Cycle Scenario!
In single cycle- only one clock tick to write, IR is not necessary

## Slide 61: Conditional Branch
Instructions are 32– bits binary encoded numbers
Programs are stored in memory — to be read or written just like data
A special register PC contains the address of the next instruction-usually the next one to the current being executed (PC  PC+4]
A special register IR contains the current instruction being executed (not always)
A branch instruction may change PC, PC  PC + ?
Branch gives the power and challenge

## Slide 62: Branch - BEQ
If (A != B) A  A + B; B  2 * B;
beq Ra Rb 2
add Ra Ra Rb
add Rb Rb Rb
PC
20
00000..0000000001
00000--0000000011
+4
IR
24
Ra
Rb
28
+2*4
Ra = Rb ?
If-else ?
beq Ra Rb 2
20
ALU
CTRL
Suppose A = 1 , B = 3
and A is in Ra and B is in Rb

## Slide 63: conditional branch- BNQ & BEQ
bne $t0, $t1, offset
if ($t0!=$t1) pcpc+4*offset
beq $t0, $t1, offset
if ($t0=$t1) pcpc+4*offset
offset is an immediate +/- value which gives a PC relative word distance
Cannot do IF- ELSE now ? : Need to study J

## Slide 64: Encoding - Conditional branch
Research shows conditional branch jumps only small distance related to current instruction position
PC related 16 bit immediate is sufficient for this
Therefore, I-type format can be used
Instructions are words- word distance is used
Should jump both sides- 2’s compliment number format used
bne $t0, $t1, 20
beq $t0, $t1, 20
05
2
3
20
bne
04
2
3
20
beq
bne
beq
000101
00010
00011
0000000000010100
000100
00010
00011
0000000000010100

## Slide 65: Encoding -Example
010000
010000
01000
000000
000000
01000
01000
00000
add
add
beq
000000
00111
00111
01000
000100
00111
01000
000000000000010
If (A != B) A  A + B; B  2 * B;
beq $7 $8 2
add $7 $7 $8
add $8 $8 $8
24
28
20
Suppose A is in $7 and B is in $8
MIPS- Assembly
bne $7, $8, Label
add $7, $7, $8 Label:
add $8, $8, $8

## Slide 66: MIPS- Assembler use LABELS
score = 0 answer =3 stAnswer =4
If (answer == stAnswer) score +=4
.globl main
.data
.text
main:
ori $t0, $0, 0
ori $t1 $0, 4
ori $t2, $0, 2
bne $t1, $t2, SKIP
addi $t0, $t0, 4
SKIP:
move $t4, $t0
bne $t1, $t2, 2
addi $t0, $t0, 4
move $t4, $t0
bne $t1, $t2, 8 ??

## Slide 67
.globl main.
main:
ori $t0, $0, 0
ori $t1 $0, 4
ori $t2, $0, 2
bne $t1, $t2, SKIP
addi $t0, $t0, 4
SKIP:
move $t4, $t0
Check PC
Check Registers
Check MIPS ISA
Check MIPS ML, and in Hex
Check SPIM code
Check for psuedo codes.

## Slide 68: Can we do IF_ELSE now?
score = 0 answer =3 stAnswer =4
If (answer == stAnswer) score +=4 else score -= 2;
.globl main
.data
.text
main:
ori $t0, $0, 0
ori $t1 $0, 4
ori $t2, $0, 2
bne $t1, $t2, SKIP
addi $t0, $t0, 4
SKIP:
addi $t0, $t0, -2 ???
bne $t1, $t2, 2
addi $t0, $t0, 4
addi $t0, $t0, -2 ???
Cannot do IF- ELSE now - why? : Need to study J

## Slide 69: Encoding -Example
00000000000000000000000000000001
$8
$7
$6
00000000000000000000000000000001
00000000000000000000000000000011
Suppose the address A1 is in PC now. The current state of the register is given on the left. What will be the state of the register when PC is A1 + 12
000100 00111 01000 0000000000000010
000000 00111 00111 00111 00000 100000
000000 01000 01000 01000 00000 100000
A1+4
A1+8
A1
??
$8
$7
$6
??
??
PC
A1

## Slide 70: Loop – Do While
t  5
S  S + t
t  t - 1
S 0
t = 0 ?
Y
N
Finally, what will be in $s0?
addi $t0, $0, 5
addi $s0, $0, 0
add $s0, $s0, $t0
addi $t0, $t0, -1
bne $t0, $0, -2

## Slide 71: Loop – Do While: FACT
t  5
S  ???
t  t - 1
S  ?
t = 0 ?
Y
N
Calculate 5!, and
leave it in $s0?
addi $t0, $0, 5
addi $s0, $0, ?
??? $s0, $s0, $t0
addi $t0, $t0, -1
bne $t0, $0, -2

## Slide 72
J- Format
Instructions
Unconditional Jumping
& IF- THEN- ELSE
& While-Do
& proc call

## Slide 73
Research shows unconditional branch jumps far distances. 16 bit offset is not sufficient
Another compromise- a new format (j-format] is introduced- opcode differentiates all 3 formats
02
000010
00000000000000000000010101
J-format
Address in j is an immediate word address-
So two 0’s should be added in last.
Yet first four bites are borrowed from PC.
Only can jump to part of RAM related to PC.
26
6
Unconditional jump – J Format
j address

## Slide 74: MIPS ISA : If-Else
if (i==j) f = g+h; else f = g-h; g = h
f, g, j in $s0, $s1, …$s4
bne $s3, $s4, 3 add $s0, $s1, $s2 j ?? [PC + 8] sub $s0, $s1, $s2 add $s1, $s2, $0
f = g - h
i== j ?
f = g + h
g = h
J ?
pc  pc + 3 * 4
pc  pc + 2 * 4
ELSE
00010110011101000000000000000110 00000010000100011001000000010000 000010000000000000000000000000100000001000010001100100000001001000000010000100000000000000010000
00010110011101000000000000000110 00000010000100011001000000010000 000010??????????????????????????0000001000010001100100000001001000000010000100000000000000010000
J – need to give almost the full address- only the first 4 bits of PC is used + last 00. 26 + 4 + 2 : bne?

## Slide 75: MIPS Assembly: If-Else
C code:
if (i==j) f = g+h; else f = g-h; g = h
f, g, … in $s0, $s1, …
Compiled MIPS code:
bne $s3, $s4, Else add $s0, $s1, $s2 j Exit Else: sub $s0, $s1, $s2 Exit: add $s1, 4S2, $0…
Assembler calculates addresses
bne $s3, $s4, 3 add $s0, $s1, $s2 j ?? sub $s0, $s1, $s2 add $s1, $s2, $0
f = g - h
i== j ?
f = g + h
g = h
J exit
EXIT
ELSE

## Slide 76: Challenge
if (A ==B) AND (B==C) // Try OR also
    code = 1
    else
    code = 2
    Draw flow graph.
    Assume A, B, C are in $t0, $t1, $t2,
    Put the code in $t3

## Slide 77: LOOP with Unconditional jump
Example loop:
while ( i !=j )
i=i+j;
loop: beq $s4, $s5, exit; add $s4, $s4, $s5 j loop exit:
i== j ?
i= i+j
J - 2
EXIT
LOOP
beq $s4, $s5, 3 add $s4, $s4, $s5 j ?? sub $s0, $s1, $s2 add $s1, $s2, $0

## Slide 78: LOOP – WHILE DO
Example loop:
while ( i !=j )
i=i+j;
beq $s4, $s5, 3 add $s4, $s4, $s5 j ??
i== j ?
i= i+j
J - 2
EXIT
LOOP
00010110100101010000000000000110 00000010100101001010100000010000 000010 ????

## Slide 79: Loop Example
C code:
while (save[i] == k) i += 1;
  i in $s3, k in $s5, address of save in $s6
Compiled MIPS code:
Loop: sll $t1, $s3, 2 add $t1, $t1, $s6 lw $t0, 0($t1) bne $t0, $s5, Exit addi $s3, $s3, 1 j Loop Exit: …

## Slide 80: Loop – While Do : eg. FACT
Calculate 5!, and put it in $s0?
addi $t0, $0, 5
addi $s0, $0, ?
Loop:
beq $t0, $0, endLoop
mul $s0, $s0, $t0
addi $t0, $t0, -1
j Loop
endLoop:

## Slide 81: BLT, BGT ? use SLT
Set result to 1 if a condition is true
  Otherwise, set to 0
slt rd, rs, rt
  if (rs < rt) rd = 1; else rd = 0;
slti rt, rs, constant
  if (rs < constant) rt = 1; else rt = 0;
Use in combination with beq, bne
  slt $t0, $s1, $s2 # if ($s1 < $s2) bne $t0, $zero, L # branch to L

## Slide 82: BLT & BGT are Pseudo codes
Why not blt, bge, etc in MIPS ISA?
Hardware for <, ≥, … slower than =, ≠
  Combining with branch involves more work per instruction, requiring a slower clock
  All instructions penalized!
beq and bne are the common case
This is a good design compromise
BLT - assembler convert it to SLT and BEQ
$1 is used by the assembler to store SLT result
Similarly BGE

## Slide 83: BLT- Branch if Less Than & BGT
blt $8, $9, label
translates to
slt $1, $8, $9
bne $1, $0, label
bgt $8, $9, label
translates to
slt $1, $8, $9
bne $1, $0, label
BLE- Branch if Less than Equal to & BGE (check whether the opposite is not true)
ble $8, $9, label
translates to
slt $1, $9, $8
beq $1, $0, label
bge $8, $9, label
translates to
slt $1, $9, $8
beq $1, $0, label

## Slide 84: Signed vs. Unsigned SLT
Signed comparison: slt, slti
Unsigned comparison: sltu, sltui
Example
  $s0 = 1111 1111 1111 1111 1111 1111 1111 1111
  $s1 = 0000 0000 0000 0000 0000 0000 0000 0001
  slt $t0, $s0, $s1 # signed
    –1 < +1  $t0 = 1
  sltu $t0, $s0, $s1 # unsigned
    +4,294,967,295 > +1  $t0 = 0

## Slide 85
PROCEDURE

## Slide 86: Procedure Calling
Steps required
  Place parameters in registers
  Transfer control to procedure
  Acquire storage for procedure
  Perform procedure’s operations
  Place result in register for caller
  Return to place of call
§2.8 Supporting Procedures in Computer Hardware

## Slide 87: Register Usage
$a0 – $a3: arguments (reg’s 4 – 7)
$v0, $v1: result values (reg’s 2 and 3)
$t0 – $t9: temporaries
  Can be overwritten by callee
$s0 – $s7: saved
  Must be saved/restored by callee
$gp: global pointer for static data (reg 28)
$sp: stack pointer (reg 29)
$fp: frame pointer (reg 30)
$ra: return address (reg 31)

## Slide 88: Procedure Call Instructions
Procedure call: jump and link (2 tasks)
jal ProcedureLabel
  Address of following instruction put in $ra
  $ra  PC + 4
  Jumps to target address
  PC  Label
Procedure return: jump register
jr $ra
  Copies $ra to program counter
  [ j Can also be used for computed jumps]
    e.g., for case/switch statements

## Slide 89: Add first n numbers (say n = 100)
.globl main
.data
.text
main:
addi $t0 , $0, 100 # $t0 <-- 100 ; used as n?
addi $t1, $0, 0 # $t1 <-- 0 ; used as count, may count downwords
addi $s0 , $0, 0 # $s0 <-- 0 ; used as intermediate sum
loop:
addi $t1, $t1, 1 # count++
add $s0, $s0, $t1 # sum += count
bne $t1, $t0, loop # if (count != 100) branch to loop
# to print sum (in $s0)
move $a0, $s0 # move the answer to $a0
li $v0, 1 # to print the bits in $a0 as integer
syscall
# to exit
li $v0, 10
syscall

## Slide 90: Add first n numbers (say n = 100)
JAVA PROGRAM, using a separate method
public void main {
  int n = 100;
  int m = addUpTo(n);
  print(m);
  }
private int addUpTo(int n) {
int sum = 0;
do {
sum = sum + n;
n--;
} while ( n != 100)
return sum;
}

## Slide 91: Add first n numbers (say n = 100)
main:
addi $t0 , $0, 100 # $t1 <-- 100 ; used as n
move $a0, $t0 # to pass n as the parameter
jal addUpTo
# to print sum (in $s0)
move $a0, $s0 # move the answer to $a0
li $v0, 1 # to print the bits in $a0 as integer
syscall
# to exit
li $v0, 10
syscall
addUpTo:
move $t0, $a0 # may avoid two moves $a0 <- $t0, $t0 <- $a0
addi $t1 , $0, 0 # $t1 <-- 0 ; used as count
addi $s0 , $0, 0 # $s0 <-- 0 ; used as intermediate sum
loop:
addi $t1, $t1, 1 # count++
add $s0, $s0, $t1 # sum += count
bne $t1, $t0, loop # if (count != 100) branch to loop
move $v0, $s0 # return answer in $v0
jr $ra

## Slide 92: find max(x,y) (say x = 10, y = 5)
JAVA PROGRAM to find max of two
public void main {
  int x = 10, y =5;
  int z = max(x, y);
  print(z);
  }
private int max(int x, int y) {
if (x > y)
return x
else
return y
}

## Slide 93: max
main: # program to print max of two numbers
addi $t0 , $0, 10 # $t1 <- 10 used as x
addi $t1 , $0, 5 # $t1 <- 5 used as y
move $a0, $t0
move $a1, $t1
jal max
# to print max(x,y) (returned in $v0)
move $a0, $v0 # move the answer to $a0
li $v0, 1 # to print the bits in $a0 as integer
syscall
# to exit
---
max:
move $t0, $a0 # may avoid two moves $a0 <- $t0, $t0 <- $a0
move $t1, $a1 # may avoid these two moves also
bgt $t0, $t1, if # if x > y goto if
move $v0, $t1 # else return y
j endIF
if:
move $v0, $t0 # return x
endIF:
jr $ra

## Slide 94: Revisit: FACT
Calculate 5!, and put it in $s0?
addi $t0, $0, 5
addi $s0, $0, ?
Loop:
beq $t0, $0, endLoop
mul $s0, $s0, $t0
addi $t0, $t0, -1
j Loop
endLoop:
int n = 5; int f = 1; while (n != 0) {
f = f * n–-
}

## Slide 95: Leaf Procedure - fact
int fact(int n) { int f=1; while (n != 0){
f = f * n-- ;
} return f; }
  Argument n in $a0
  Call jal fact
  Result in $v0

## Slide 96: FACT as Leaf Procedure
Calculate 5!, and put it in $s0?
addi $t0, $0, 5
move $a0, $t0 # need not to save any $t’s
jal FACT
move $s0, $v0
FACT:
addi $s0, $0, 1 # need not to save any $s’s, or $a0
Loop:
beq $a0, $0, endLoop
mul $s0, $s0, $t0
addi $a0, $a0, -1
j Loop
endLoop:
move $v0, $s0 # need not to save the $ra / jal is not called
jr $ra

## Slide 97: Memory Layout
Text: program code
Static data: global variables
  e.g., static variables in C, constant arrays and strings
  $gp initialized to address allowing ±offsets into this segment
Dynamic data: heap
  E.g., malloc in C, new in Java
Stack: automatic storage

## Slide 98: Local Data on the Stack
Local data allocated by callee
  e.g., C automatic variables
Procedure frame (activation record)
  Used by some compilers to manage stack storage

## Slide 99: Leaf Procedure Example
int leaf_example (int g, h, i, j) { int f; f = (g + h) - (i + j); return f; }
  Arguments g, …, j in $a0, …, $a3
  Call jal leaf
  f in $s0 (hence, need to save $s0 on stack)
  Do calculation
  Restore $s0
  return
  Result in $v0

## Slide 100: Leaf- Procedure Example
Complete!

## Slide 101: Non-Leaf Procedures
Procedures that call other procedures
For nested call, caller needs to save on the stack:
  Its return address
  Any arguments and temporaries needed after the call
Restore from the stack after the call

## Slide 102: Non-Leaf Procedure Example
assign n: make sure n >= 0
call fact(n);
int fact (int n) { int f = 1; if (n = 0) return f; else return n * fact(n - 1); }
  Argument n in $a0
  Result in $v0

## Slide 103: Non-Leaf: FACT recursive
fact: bne $a0, $0, L1 # test for n = 0 addi $v0, $zero, 1 # if so, result is 1 addi $sp, $sp, 8 # pop 2 items from stack jr $ra # and return L1: #else prepare for recursive call
addi $sp, $sp, -8 # adjust stack for 2 items sw $ra, 4($sp) # save return address sw $a0, 0($sp) # save argument addi $a0, $a0, -1 # decrement n jal fact # recursive call (fact (n-1) lw $a0, 0($sp) # restore original n lw $ra, 4($sp) # restore return address addi $sp, $sp, 8 # pop 2 items from stack mul $v0, $a0, $v0 # multiply to get result jr $ra # and return

## Slide 104: SPIM System Call Codes
Service | Code (put in $v0) | Arguments | Result
print_int | 1 | $a0=integer | 
print_float | 2 | $f12=float | 
print_double | 3 | $f12=double | 
print_string | 4 | $a0=addr. of string | 
read_int | 5 |  | int in $v0
read_float | 6 |  | float in $f0
read_double | 7 |  | double in $f0
read_string | 8 | $a0=buffer, $a1=length | 
sbrk | 9 | $a0=amount | addr in $v0
exit | 10 |  | 

## Slide 105: Character Data
Byte-encoded character sets
  ASCII: 128 characters
    95 graphic, 33 control
  Latin-1: 256 characters
    ASCII, +96 more graphic characters
Unicode: 32-bit character set
  Used in Java, C++ wide characters, …
  Most of the world’s alphabets, plus symbols
  UTF-8, UTF-16: variable-length encodings
§2.9 Communicating with People

## Slide 106: Byte/Halfword Operations
Could use bitwise operations
MIPS byte/halfword load/store
  String processing is a common case
lb rt, offset(rs) lh rt, offset(rs)
  Sign extend to 32 bits in rt
lbu rt, offset(rs) lhu rt, offset(rs)
  Zero extend to 32 bits in rt
sb rt, offset(rs) sh rt, offset(rs)
  Store just rightmost byte/halfword

## Slide 107: 32-bit Constants
0000 0000 0111 1101 0000 0000 0000 0000
Most constants are small
  16-bit immediate is sufficient
For the occasional 32-bit constant
lui rt, constant
  Copies 16-bit constant to left 16 bits of rt
  Clears right 16 bits of rt to 0
lhi $s0, 61
0000 0000 0111 1101 0000 1001 0000 0000
ori $s0, $s0, 2304
§2.10 MIPS Addressing for 32-Bit Immediates and Addresses

## Slide 108: Branch Addressing
Branch instructions specify
  Opcode, two registers, target address
Most branch targets are near branch
  Forward or backward
op
rs
rt
constant or address
6 bits
5 bits
5 bits
16 bits
PC-relative addressing
  Target address = PC + offset × 4
  PC already incremented by 4 by this time

## Slide 109: Jump Addressing
Jump (j and jal) targets could be anywhere in text segment
  Encode full address in instruction
op
address
6 bits
26 bits
(Pseudo)Direct jump addressing
  Target address = PC31…28 : (address × 4)

## Slide 110: Target Addressing Example
Loop code from earlier example
  Assume Loop at location 80000
Loop: sll $t1, $s3, 2 | 80000 | 0 | 0 | 19 | 9 | 4 | 0
add $t1, $t1, $s6 | 80004 | 0 | 9 | 22 | 9 | 0 | 32
lw $t0, 0($t1) | 80008 | 35 | 9 | 8 | 0 |  | 
bne $t0, $s5, Exit | 80012 | 5 | 8 | 21 | 2 |  | 
addi $s3, $s3, 1 | 80016 | 8 | 19 | 19 | 1 |  | 
j Loop | 80020 | 2 | 20000 |  |  |  | 
Exit: … | 80024 |  |  |  |  |  | 

## Slide 111: Branching Far Away
If branch target is too far to encode with 16-bit offset, assembler rewrites the code
Example
  beq $s0,$s1, L1
  ↓
  bne $s0,$s1, L2 j L1 L2: …

## Slide 112: Addressing Mode Summary

## Slide 113: Translation and Startup
Many compilers produce object modules directly
Static linking
§2.12 Translating and Starting a Program

## Slide 114: Assembler Pseudoinstructions
Most assembler instructions represent machine instructions one-to-one
Pseudoinstructions: figments of the assembler’s imagination
move $t0, $t1 → add $t0, $zero, $t1
blt $t0, $t1, L → slt $at, $t0, $t1 bne $at, $zero, L
  $at (register 1): assembler temporary

## Slide 115: Producing an Object Module
Assembler (or compiler) translates program into machine instructions
Provides information for building a complete program from the pieces
  Header: described contents of object module
  Text segment: translated instructions
  Static data segment: data allocated for the life of the program
  Relocation info: for contents that depend on absolute location of loaded program
  Symbol table: global definitions and external refs
  Debug info: for associating with source code

## Slide 116: Linking Object Modules
Produces an executable image
  1. Merges segments
  2. Resolve labels (determine their addresses)
  3. Patch location-dependent and external refs
Could leave location dependencies for fixing by a relocating loader
  But with virtual memory, no need to do this
  Program can be loaded into absolute location in virtual memory space

## Slide 117: Loading a Program
Load from image file on disk into memory
  1. Read header to determine segment sizes
  2. Create virtual address space
  3. Copy text and initialized data into memory
    Or set page table entries so they can be faulted in
  4. Set up arguments on stack
  5. Initialize registers (including $sp, $fp, $gp)
  6. Jump to startup routine
    Copies arguments to $a0, … and calls main
    When main returns, do exit syscall

## Slide 118: Dynamic Linking
Only link/load library procedure when it is called
  Requires procedure code to be relocatable
  Avoids image bloat caused by static linking of all (transitively) referenced libraries
  Automatically picks up new library versions

## Slide 119: Lazy Linkage
Indirection table
Stub: Loads routine ID, Jump to linker/loader
Linker/loader code
Dynamically mapped code

## Slide 120: Starting Java Applications
Simple portable instruction set for the JVM
Interprets bytecodes
Compiles bytecodes of “hot” methods into native code for host machine

## Slide 121: Effect of Compiler Optimization
Compiled with gcc for Pentium 4 under Linux

## Slide 122: Effect of Language and Algorithm

## Slide 123: Lessons Learnt
Instruction count and CPI are not good performance indicators in isolation
Compiler optimizations are sensitive to the algorithm
Java/JIT compiled code is significantly faster than JVM interpreted
  Comparable to optimized C in some cases
Nothing can fix a dumb algorithm!

## Slide 124: CAN SKIP THE REST

## Slide 125: Arrays vs. Pointers
Array indexing involves
  Multiplying index by element size
  Adding to array base address
Pointers correspond directly to memory addresses
  Can avoid indexing complexity
§2.14 Arrays versus Pointers

## Slide 126: Example: Clearing and Array
clear1(int array[], int size) { int i; for (i = 0; i < size; i += 1) array[i] = 0; } | clear2(int *array, int size) { int *p; for (p = &array[0]; p < &array[size]; p = p + 1) *p = 0; }
move $t0,$zero # i = 0 loop1: sll $t1,$t0,2 # $t1 = i * 4 add $t2,$a0,$t1 # $t2 = # &array[i] sw $zero, 0($t2) # array[i] = 0 addi $t0,$t0,1 # i = i + 1 slt $t3,$t0,$a1 # $t3 = # (i < size) bne $t3,$zero,loop1 # if (…) # goto loop1 | move $t0,$a0 # p = & array[0] sll $t1,$a1,2 # $t1 = size * 4 add $t2,$a0,$t1 # $t2 = # &array[size] loop2: sw $zero,0($t0) # Memory[p] = 0 addi $t0,$t0,4 # p = p + 4 slt $t3,$t0,$t2 # $t3 = #(p<&array[size]) bne $t3,$zero,loop2 # if (…) # goto loop2

## Slide 127: Comparison of Array vs. Ptr
Multiply “strength reduced” to shift
Array version requires shift to be inside loop
  Part of index calculation for incremented i
  c.f. incrementing pointer
Compiler can achieve same effect as manual use of pointers
  Induction variable elimination
  Better to make program clearer and safer

## Slide 128: ARM & MIPS Similarities
ARM: the most popular embedded core
Similar basic set of instructions to MIPS
§2.16 Real Stuff: ARM Instructions
 | ARM | MIPS
Date announced | 1985 | 1985
Instruction size | 32 bits | 32 bits
Address space | 32-bit flat | 32-bit flat
Data alignment | Aligned | Aligned
Data addressing modes | 9 | 3
Registers | 15 × 32-bit | 31 × 32-bit
Input/output | Memory mapped | Memory mapped

## Slide 129: Compare and Branch in ARM
Uses condition codes for result of an arithmetic/logical instruction
  Negative, zero, carry, overflow
  Compare instructions to set condition codes without keeping the result
Each instruction can be conditional
  Top 4 bits of instruction word: condition value
  Can avoid branches over single instructions

## Slide 130: Instruction Encoding

## Slide 131: The Intel x86 ISA
Evolution with backward compatibility
  8080 (1974): 8-bit microprocessor
    Accumulator, plus 3 index-register pairs
  8086 (1978): 16-bit extension to 8080
    Complex instruction set (CISC)
  8087 (1980): floating-point coprocessor
    Adds FP instructions and register stack
  80286 (1982): 24-bit addresses, MMU
    Segmented memory mapping and protection
  80386 (1985): 32-bit extension (now IA-32)
    Additional addressing modes and operations
    Paged memory mapping as well as segments
§2.17 Real Stuff: x86 Instructions

## Slide 132: The Intel x86 ISA
Further evolution…
  i486 (1989): pipelined, on-chip caches and FPU
    Compatible competitors: AMD, Cyrix, …
  Pentium (1993): superscalar, 64-bit datapath
    Later versions added MMX (Multi-Media eXtension) instructions
    The infamous FDIV bug
  Pentium Pro (1995), Pentium II (1997)
    New microarchitecture (see Colwell, The Pentium Chronicles)
  Pentium III (1999)
    Added SSE (Streaming SIMD Extensions) and associated registers
  Pentium 4 (2001)
    New microarchitecture
    Added SSE2 instructions

## Slide 133: The Intel x86 ISA
And further…
  AMD64 (2003): extended architecture to 64 bits
  EM64T – Extended Memory 64 Technology (2004)
    AMD64 adopted by Intel (with refinements)
    Added SSE3 instructions
  Intel Core (2006)
    Added SSE4 instructions, virtual machine support
  AMD64 (announced 2007): SSE5 instructions
    Intel declined to follow, instead…
  Advanced Vector Extension (announced 2008)
    Longer SSE registers, more instructions
If Intel didn’t extend with compatibility, its competitors would!
  Technical elegance ≠ market success

## Slide 134: Basic x86 Registers

## Slide 135: Basic x86 Addressing Modes
Two operands per instruction
Source/dest operand | Second source operand
Register | Register
Register | Immediate
Register | Memory
Memory | Register
Memory | Immediate
Memory addressing modes
  Address in register
  Address = Rbase + displacement
  Address = Rbase + 2scale × Rindex (scale = 0, 1, 2, or 3)
  Address = Rbase + 2scale × Rindex + displacement

## Slide 136: x86 Instruction Encoding
Variable length encoding
  Postfix bytes specify addressing mode
  Prefix bytes modify operation
    Operand length, repetition, locking, …

## Slide 137: Implementing IA-32
Complex instruction set makes implementation difficult
  Hardware translates instructions to simpler microoperations
    Simple instructions: 1–1
    Complex instructions: 1–many
  Microengine similar to RISC
  Market share makes this economically viable
Comparable performance to RISC
  Compilers avoid complex instructions

## Slide 138: ARM v8 Instructions
In moving to 64-bit, ARM did a complete overhaul
ARM v8 resembles MIPS
  Changes from v7:
    No conditional execution field
    Immediate field is 12-bit constant
    Dropped load/store multiple
    PC is no longer a GPR
    GPR set expanded to 32
    Addressing modes work for all word sizes
    Divide instruction
    Branch if equal/branch if not equal instructions
§2.18 Real Stuff: ARM v8 (64-bit) Instructions

## Slide 139: Fallacies
Powerful instruction  higher performance
  Fewer instructions required
  But complex instructions are hard to implement
    May slow down all instructions, including simple ones
  Compilers are good at making fast code from simple instructions
Use assembly code for high performance
  But modern compilers are better at dealing with modern processors
  More lines of code  more errors and less productivity
§2.19 Fallacies and Pitfalls

## Slide 140: Fallacies
Backward compatibility  instruction set doesn’t change
  But they do accrete more instructions
x86 instruction set

## Slide 141: Pitfalls
Sequential words are not at sequential addresses
  Increment by 4, not by 1!
Keeping a pointer to an automatic variable after procedure returns
  e.g., passing pointer back via an argument
  Pointer becomes invalid when stack popped

## Slide 142: Concluding Remarks
Design principles
  1. Simplicity favors regularity
  2. Smaller is faster
  3. Make the common case fast
  4. Good design demands good compromises
Layers of software/hardware
  Compiler, assembler, hardware
MIPS: typical of RISC ISAs
  c.f. x86
§2.20 Concluding Remarks

## Slide 143: Concluding Remarks
Measure MIPS instruction executions in benchmark programs
  Consider making the common case fast
  Consider compromises
Instruction class | MIPS examples | SPEC2006 Int | SPEC2006 FP
Arithmetic | add, sub, addi | 16% | 48%
Data transfer | lw, sw, lb, lbu, lh, lhu, sb, lui | 35% | 36%
Logical | and, or, nor, andi, ori, sll, srl | 12% | 4%
Cond. Branch | beq, bne, slt, slti, sltiu | 34% | 8%
Jump | j, jr, jal | 2% | 0%

## Slide 144: String Copy Example
C code (naïve):
  Null-terminated string
void strcpy (char x[], char y[]) { int i; i = 0; while ((x[i]=y[i])!='\0') i += 1; }
  Addresses of x, y in $a0, $a1
  i in $s0

## Slide 145: String Copy Example
MIPS code:
strcpy: addi $sp, $sp, -4 # adjust stack for 1 item sw $s0, 0($sp) # save $s0 add $s0, $zero, $zero # i = 0 L1: add $t1, $s0, $a1 # addr of y[i] in $t1 lbu $t2, 0($t1) # $t2 = y[i] add $t3, $s0, $a0 # addr of x[i] in $t3 sb $t2, 0($t3) # x[i] = y[i] beq $t2, $zero, L2 # exit loop if y[i] == 0 addi $s0, $s0, 1 # i = i + 1 j L1 # next iteration of loop L2: lw $s0, 0($sp) # restore saved $s0 addi $sp, $sp, 4 # pop 1 item from stack jr $ra # and return

## Slide 146: C Sort Example
Illustrates use of assembly instructions for a C bubble sort function
Swap procedure (leaf)
  void swap(int v[], int k) { int temp; temp = v[k]; v[k] = v[k+1]; v[k+1] = temp; }
  v in $a0, k in $a1, temp in $t0
§2.13 A C Sort Example to Put It All Together

## Slide 147: The Procedure Swap
swap: sll $t1, $a1, 2 # $t1 = k * 4
add $t1, $a0, $t1 # $t1 = v+(k*4)
# (address of v[k])
lw $t0, 0($t1) # $t0 (temp) = v[k]
lw $t2, 4($t1) # $t2 = v[k+1]
sw $t2, 0($t1) # v[k] = $t2 (v[k+1])
sw $t0, 4($t1) # v[k+1] = $t0 (temp)
jr $ra # return to calling routine

## Slide 148: The Sort Procedure in C
Non-leaf (calls swap)
  void sort (int v[], int n)
  {
  int i, j;
  for (i = 0; i < n; i += 1) {
  for (j = i – 1;
  j >= 0 && v[j] > v[j + 1];
  j -= 1) {
  swap(v,j);
  }
  }
  }
  v in $a0, k in $a1, i in $s0, j in $s1

## Slide 149: The Procedure Body
move $s2, $a0 # save $a0 into $s2
move $s3, $a1 # save $a1 into $s3
move $s0, $zero # i = 0
for1tst: slt $t0, $s0, $s3 # $t0 = 0 if $s0 ≥ $s3 (i ≥ n)
beq $t0, $zero, exit1 # go to exit1 if $s0 ≥ $s3 (i ≥ n)
addi $s1, $s0, –1 # j = i – 1
for2tst: slti $t0, $s1, 0 # $t0 = 1 if $s1 < 0 (j < 0)
bne $t0, $zero, exit2 # go to exit2 if $s1 < 0 (j < 0)
sll $t1, $s1, 2 # $t1 = j * 4
add $t2, $s2, $t1 # $t2 = v + (j * 4)
lw $t3, 0($t2) # $t3 = v[j]
lw $t4, 4($t2) # $t4 = v[j + 1]
slt $t0, $t4, $t3 # $t0 = 0 if $t4 ≥ $t3
beq $t0, $zero, exit2 # go to exit2 if $t4 ≥ $t3
move $a0, $s2 # 1st param of swap is v (old $a0)
move $a1, $s1 # 2nd param of swap is j
jal swap # call swap procedure
addi $s1, $s1, –1 # j –= 1
j for2tst # jump to test of inner loop
exit2: addi $s0, $s0, 1 # i += 1
j for1tst # jump to test of outer loop
Pass params & call
Move params
Inner loop
Outer loop
Inner loop
Outer loop

## Slide 150: The Full Procedure
sort: addi $sp,$sp, –20 # make room on stack for 5 registers
sw $ra, 16($sp) # save $ra on stack
sw $s3,12($sp) # save $s3 on stack
sw $s2, 8($sp) # save $s2 on stack
sw $s1, 4($sp) # save $s1 on stack
sw $s0, 0($sp) # save $s0 on stack
… # procedure body
…
exit1: lw $s0, 0($sp) # restore $s0 from stack
lw $s1, 4($sp) # restore $s1 from stack
lw $s2, 8($sp) # restore $s2 from stack
lw $s3,12($sp) # restore $s3 from stack
lw $ra,16($sp) # restore $ra from stack
addi $sp,$sp, 20 # restore stack pointer
jr $ra # return to calling routine

## Slide 151: Synchronization
Two processors sharing an area of memory
  P1 writes, then P2 reads
  Data race if P1 and P2 don’t synchronize
    Result depends of order of accesses
Hardware support required
  Atomic read/write memory operation
  No other access to the location allowed between the read and write
Could be a single instruction
  E.g., atomic swap of register ↔ memory
  Or an atomic pair of instructions
§2.11 Parallelism and Instructions: Synchronization

## Slide 152: Synchronization in MIPS
Load linked: ll rt, offset(rs)
Store conditional: sc rt, offset(rs)
  Succeeds if location not changed since the ll
    Returns 1 in rt
  Fails if location is changed
    Returns 0 in rt
Example: atomic swap (to test/set lock variable)
  try: add $t0,$zero,$s4 ;copy exchange value
  ll $t1,0($s1) ;load linked
  sc $t0,0($s1) ;store conditional
  beq $t0,$zero,try ;branch store fails
  add $s4,$zero,$t1 ;put load value in $s4